## Slide 1
Software-Defined Radios platforms
Gara Quintana Díaz
PhD candidate - SmallSat Lab

## Slide 2: Table of Contents
GomSpace SDR
USRP E310
USRP N210
LimeSDR-USB
LimeSDR-mini
RTL-SDR
SWIFT-UTX
SWIFT-SLX
SWIFT-WRX
FunCube Dongle Pro
FunCube Dongle ProPlus
ASTROSDR
EPIQ solutions Matchtiq
EPIQ Matchtiq S10-S12
EPIQ Bitshark Express Rx
BladeRF
HackRF One

## Slide 3: 1. GomSpace
GomSpace SDR
NanoMind Z7000: FPGA module
NanoDock SDR
NanoCom TR-600: transceiver
Cost: 30 000 €
Dim.: 0.3U
Weight: 100 g
Power: 3 W idle
Space proven
General specifications

## Slide 4: 1. GomSpace
NanoMind Z7000: FPGA module
NanoDock SDR
NanoCom TR-600: transceiver
Centralized 40 MHz clock
Fits standard PC104
MicroSD card connector
USB to UART console
Op. temp.: -20°C to +60°C
Mass: 74.2 g
Xilinx Zynq 7030 SoC
Dual ARM Cortex A9 MPCore up to 800 MHz
FPGA– 125K logic cells
1 GB DDR3 RAM
32 GB storage
Freq: 70 MHz to 6 GHz
Up to 56 MHz bandwidth
2 x TX/RX channels
Chip: AD9361
  TX: 47-70 MHz
  RX:70 M-6 GHz
  TDD, FDD
  F=2 dB at 800 MHz LO
RF capabilities
Processing
Software/framework
Linux OS

## Slide 5: 1. GomSpace
NanoMind Z7000: FPGA module
NanoDock SDR
NanoCom TR-600: transceiver

## Slide 6: 2. USRP E310
Cost: 3 000€
Dim.: 133 x 68 x 26.4 mm
Weight: 375 g
Power: 2-6 W
Not space proven
RF capabilities
Processing
Software/framework
General specifications
Xilinx Zynq 7020 SoC 1
ARM Cortex A9 866 MHz dual-core
7 Series FPGA
1 GB DDR3 RAM for ARM
512 MB DDR3 RAM for FPGA
Up to 10 MS/s to ARM
Freq: 70 MHz to 6 GHz
Up to 56 MHz bandwidth
2 RX, 2 TX
Filter banks
Chip: AD93612
  TX: 47-70 MHz
  RX:70 M-6 GHz
  TDD, FDD
  F=2 dB at 800 MHz LO
UHD version 3.8.0/+
RFNOC
GNU Radio
C/C++
Python
1 -Aerospace & Michigan
-Surrey
2 -Surrey
RF capabilities
Software/framework

## Slide 7: 2. USRP E310

## Slide 8: 2. USRP E310

## Slide 9: 3. USRP N210
Cost: 1 600 €
Dim.: 220 x 160 x 50 mm
Weight: 1 200 g
Current consump.: 1.3 A
Not space proven
RF capabilities
Processing
Software/framework
General specifications
Spartan 3A1-DSP 3400 FPGA
Microblaze and picoblaze cores
1 MB High-Speed SRAM
DDC/DUC with 25 mHz Resolution
Freq: DC to 6 GHz
Dual 100 MS/s, 14-bit ADC
Dual 400 MS/s, 16-bit DAC
w/WBX Daughter board
  Power output: 15 dBm
  IIP3: 0 dBm
  RX noise figure: 5 dB
GNU Radio
LabVIEW™
Simulink™
-Carolina & North Dakota
-Warsaw
-Bologna
1 Worcester

## Slide 10: 3. USRP N210

## Slide 11: 4. LimeSDR-USB
Cost: 200 €
Dim.: 60 x 100 mm
Weight: 100-200 g
Power:
Not space proven
RF capabilities
Processing
Software/framework
General specifications
Altera1 Cyclone IV EP4CE40F23C8N
256 MBytes DDR2 SDRAM
Freq: 0.1 MHz to 3.8 GHz
Up to 61.44 MHz bandwidth
2 TX x 2 RX channels
DAC: 640 MHz
ADC: 160 MHz
Power output: up to 10 dBm
Chip: LMS7002M FPRF
  Noise figure: 2-3.5 dB
  RX control gain: 70 dB
GNU Radio
1 Istanbul

## Slide 12: 4. LimeSDR-USB

## Slide 13: 5. LimeSDR-mini
Cost: 84 €
Dim.: 69 x 31.4 mm
Weight:
Power:
Not space proven
RF capabilities
Processing
Software/framework
General specifications
FPGA: Altera MAX 10 (10M16SAU169C8G)
EEPROM memory: 2 x 128 KB for RF
1 x 4 MB flash memory
Freq: 0.01 MHz to 3.5 GHz
Up to 30.72 MHz bandwidth
1 TX x 1 RX channels
DAC: 640 MHz
ADC: 160 MHz
Power output: up to 10 dBm
Chip: LMS7002M FPRF
  Noise figure: 2-3.5 dB
  RX control gain: 70 dB
GNU Radio
Differences
FPGA
Frequency
BW
Sample rate
No. Channels
No. Logic gates
Size
Price
SMA connections

## Slide 14: 5. LimeSDR-mini

## Slide 15: 6. RTL-SDR Blog V3
Cost: 26 €
Dim.: 45 x 55 x 15 mm
Weight:
Power: Not space proven
RF capabilities
Processing
Software/framework
General specifications
Freq: 0.5 MHz to 1.766 GHz
Up to 2.4 MHz bandwidth
DVB-T, DAB, FM, SDR
Chip: R820T2
  Noise figure: 3.5 dB
Compatible with most OS
GNU Radio
UPCatalunya

## Slide 16: 6. RTL-SDR Blog V3

## Slide 17: 7. SWIFT-UTX
Cost: Dim.: 86 x 45 mm (0.25U)
Weight:
Power: 7.5-40 W
Not space proven (designed for CubeSats)
RF capabilities
Processing
Software/framework
General specifications
Freq: 200 – 500 MHz,
7 MHz bandwidth
SWIFT-LINK: link-layer SW
Lacking information

## Slide 18: 7. SWIFT-UTX

## Slide 19: 8. SWIFT-SLX
Cost:
Dim.: 86 x 25-35 mm (0.25U)
Weight: 200-250 g (excluding diplexer)
Power: 2.5-15 W (modes)
Designed for pico and nanosats
RF capabilities
Processing
Software/framework
General specifications
Freq: 1.5 – 2.5 GHz (TX), 1 -4 GHz (RX)
Up to 56 MHz bandwidth
2 TX and 4 RX
Noise figure: 0.75 dB
Optional diplexer for full-duplex
SWIFT-LINK
Lacking information

## Slide 20: 8. SWIFT-SLX

## Slide 21: 9. SWIFT-WRX
Cost:
Dim.:
Weight:
Power:
Designed for CubeSats
RF capabilities
Processing
Software/framework
General specifications
Freq: 50 MHz to 7 GHz
Lacking information

## Slide 22: 10. FunCube Dongle Pro
Cost: 135 €
Dim.:
Weight:
Power:
Not space proven
RF capabilities
Processing
Software/framework
General specifications
PIC24FJ32GB002 processor
Freq: 0.64 MHz-1.1 GHz (TX), 1.27 - 1.7 GHz (RX)
Up to 96 KHz bandwidth
Sample rate: 96 KHz
Flexible IF amplifier and channel filter
USB Dongle powered by PC’s USB port
Compatible with most OS
Controlled by its own µC and OS
Programmed by PC

## Slide 23: 10. FunCube Dongle Pro

## Slide 24: 11. FunCube Dongle Pro+
Cost: 167 €
Dim.:
Weight:
Power: Not space proven
RF capabilities
Processing
Software/framework
General specifications
Freq: 150 - 260 GHz (TX), 410 – 2.15 GHz (RX)
Up to 56 MHz bandwidth
Sample rate: 192 KHz

## Slide 25: 12. ASTROSDR
Cost:
Dim.: 90 x 90 mm
Weight: 95 g (without heatsink or daughter card
Power: 4-40 W
Space Plug-and-Play
RF capabilities
Processing
Software/framework
General specifications
Xilinx Zynq Z-7045
Dual-core ARM Cortex A9 with NEON, up to 800 MHz
Kintex-7 FPGA
512 Mbyte DDR3 RAM
2 GByte Flash
Freq: 70 MHz to 6 GHz
56 MHz (single) and 25 MHz (dual) bandwidth
Dual RX and dual TX
Chip: AD9361
  TX: 47-70 MHz
  RX:70 M-6 GHz
  TDD, FDD
  F=2 dB at 800 MHz LO
Embedded linux

## Slide 26: 12. ASTROSDR

## Slide 27: 13. EPIQ Solutions Matchstiq
Cost: 3 900 €
Dim.: 112 x 50.8 x 36.3 mm
Weight: 142 g
Power: < 3 W
Not space proven
RF capabilities
Processing
Software/framework
General specifications
Xilinx Spartan®6 LX45T FPGA
Quad-core ARM Cortex A9 CPU
32 GB non-volatile memory
512 MB LPDDR2 RAM
Freq: 70 MHz to 6 GHz
1.5-28 MHz bandwidth
Zero-IF (direct conversion)
Sampling rate: Up to 40 MHz
Output power: 10 dBm
Noise figure: < 8 dB
SDK available
Runs Linux
Max 10

## Slide 28: 13. EPIQ Solutions Matchstiq

## Slide 29: 14. Matchtiq S10-S12
Cost: 3 900€
Dim.: 112 x 50.8 x 36.3 mm
Weight: 160-215 g
Power: 2-6 W
Not space proven
RF capabilities
Processing
Software/framework
General specifications
Xilinx Zynq 7020 SoC
ARM Cortex A9 866 MHz dual-core
1 GB RAM
2 GB FLASH
Freq: 1-70 MHz to 6 GHz
Up to 50 MHz bandwidth
Output power: 10-13 dBm
Sampling rate: Up to 61.44 MSps
Chip: AD9361
  TX: 47-70 MHz
  RX:70 M-6 GHz
  TDD, FDD
  F=2 dB at 800 MHz LO
Runs Linux

## Slide 30: 14. Matchtiq S10-S12

## Slide 31: 14. Matchtiq S10-S12

## Slide 32: 15. EPIQ Bitshark Express Rx
Cost: 3 650 – 5320 €
Dim.:
Weight:
Power:
Not space proven
RF capabilities
Processing
Software/framework
General specifications
Xilinx® Spartan®-6 LX45T FPGA
128MB DDR3 Memory
Freq: 300 MHz to 4 GHz
Up to 50 MHz bandwidth
Smapling rate 105 MSps
Windows and Linux compatible

## Slide 33: 15. EPIQ Bitshark Express Rx

## Slide 34: 16. BladeRF
Cost: 360 €
Dim.: 87 x 131 x 18 mm
Weight:
Power:
Not space proven
RF capabilities
Processing
Software/framework
General specifications
Altera Cyclone IV
ARM926EJ-S
Freq: 300 MHz to 3.8 GHz
Output power: 6 dBm
Chip: LMS6002D
  TX: 47-70 MHz
  RX:70 M-6 GHz
  BW: Up to 28 MHz
  TDD, FDD
  F=3.5-10 dB
GNU Radio
Compatible with most OS

## Slide 35: 16. BladeRF

## Slide 36: 17. HACKRF One
Cost: 280€
Dim.: 120 x 75 mm
Weight:
Power:
Not space proven
RF capabilities
Processing
Software/framework
General specifications
LPC43xx ARM Cortex-M4 µC
Freq: 1 MHz to 6 GHz
1.75 – 28 MHz bandwidth
Sample rate: 2-20 Msps
Output power: -10 to 15 dBm depending on freq.
Chip: MAX2837 transceiver
  2.3 - 2.7 GHz
  Noise figure: 2.3 dB
GNU Radio

## Slide 37: 17. HACKRF One

## Slide 38: Conclusions
17 SDR platforms studied
  Cost: 26-30,000 €
  Space proven: 2
  Weights: 95 g-1.2 Kg (most of them don’t include cases)
  Power consumption: 3 W (idle)-40 W
  Processing units
    4 Xilinx Zynq
    2 Altera Cyclone IV
  Transceiver chips
    4 AD4361
    3 Lime chips