## Slide 1: Inspection Planning in the Marine Sector: a Case Study of a Hydrogen-Fueled Fishing Vessel
Leonardo Giannini – 27/04/2023

## Slide 2: OMAE 2023 – 42nd International Conference on Ocean, Offshore & Arctic Engineering
Melbourne Convention and Exhibition Centre, Melbourne, Australia [1]
June 11-16, 2023
Notes: This is an extended version of the pres. For OMAE – where is it – first time – suggestions are appreciated

## Slide 3: Structure of the presentation
1. Introduction: why this study?
2. A hydrogen-fuelled fishing vessel
3. Risk-Based Inspection for hydrogen technologies
4. Results and Discussion

## Slide 4
Structure of the presentation
1. Introduction: why this study?
2. A hydrogen-fuelled fishing vessel
3. Risk-Based Inspection for hydrogen technologies
5. Results and Discussion
4. Methodology
Notes: Just talk about the structure point by point

## Slide 5: Introduction: why this study?
Hydrogen implementation on fishing vessels:
Reduction of
GHG emissions
Improvement of fishermen working conditions
Less volume/weight than batteries
Notes: Just read

## Slide 6
Introduction: why this study?
Hydrogen implementation on fishing vessels:
Shipping, including fishing, contributed to 2.89% of global greenhouse gas (GHG) emissions in 2018 [2]. In 2021, the Norwegian fishing fleet emitted approximately 855,000 tons of GHGs, which accounts for 1.3% of the total pollutant emissions in Norway [3].
Notes: Environmental relevance

## Slide 7
Introduction: why this study?
Hydrogen implementation on fishing vessels:
Drastic noise and vibrations reduction on board with respect to conventional combustion engines [4].
Notes: Improve of conditions on fishing vessels

## Slide 8
Introduction: why this study?
Hydrogen implementation on fishing vessels:
Batteries weight, occupied volume, relatively high costs, and limited energy storage capacity are critical downsides. Moreover, fishing vessels are often designed and optimized to achieve the best possible load capacity, which could drastically be reduced by the presence of batteries [4].
Notes: Comparison with batteries

## Slide 9: A hydrogen-fuelled fishing vessel
Characteristics:
13 m fishing vessel
Hydrogen-fed fuel cells for power
160 kg of hydrogen
18 h working session
3 h: Time required for steaming to the fishing areas
12 h: Time required for fishing
3 h: Time required to return to the port area
Figure 1: Qualitative description of the fishing boat, adapted from [4] and illustrated by GOT Skogsøy AS
Project led by SINTEF Ocean [4], where technical, economic, and environmental aspects related to the utilization of hydrogen and ammonia-fed fuel cells onboard a fishing vessel were studied.
Notes: Talk about the case study – sintef ocean – techno-economical and environmental analysis – characteristics of the vessel

## Slide 10: A hydrogen-fuelled fishing vessel
Figure 2: Hydrogen storage systems and piping from [4]
Notes: This is a P&ID of the storage system of hydrogen – talk about the element – say that the pressure is important before moving on – for the sake of brevity we chose the hydrogen cylinders

## Slide 11: A hydrogen-fuelled fishing vessel
molecule
Van der Waals forces – Physisorption [5]
Molecular dissociation – Chemisorption [5]
Diffusion - Absorption
Steel structure
Notes: Pressure driven hydrogen uptake – explain the steps

## Slide 12: Risk-Based Inspection
RBI provides a vehicle for continuously improving the inspection of facilities and systematically reducing pressure boundary failures [6]
Risk Assessment and Ranking
Inspection Plan
Data Gathering
Mitigation Activities and Reassessment
Starting point
RBI
Notes: Before showing the results, explain what RBI is – definition – maybe of you already know so I’ll keep it short.

## Slide 13
Risk-Based Inspection
Risk Assessment and Ranking
Inspection and Mitigation Activities
Data Gathering
Environmental Conditions
Operative Conditions
Equipment Age and History
Probability of Failure
Consequence of Failure
Maintenance
Substitutions
Planning of Future Inspections
Notes: Talk about the points

## Slide 14
Risk Assessment and Ranking
Probability of Failure
Consequence of Failure
Risk-Based Inspection
Probability of Failure
: generic failure frequency
: damage factor
: Management system factor
Consequence of failure
Example of consequence categories. Notice that ranges need to be adjusted for the considered plant or unit.
Notes: Element of the formula – The GFF of a component type is estimated using records from all plants within a company or from various
plants within an industry, from literature sources, and from commercial reliability databases - FSM is an adjustment factor that accounts for the influence of the facility’s
management system on the mechanical integrity of the plant equipment -

## Slide 15
Risk-Based Inspection
The Role of Hydrogen in API RBI 581 [7]
Damage Mechanisms API581 |  | Hydrogen
1 | Thinning | NO
2 | Component Lining | NO
3 | SCC – Caustic Cracking | NO
4 | SCC – Amine Cracking | NO
5 | SCC – Sulfide Stress Cracking | YES
6 | SCC – HIC/SOHIC-H2S | YES
7 | SCC – Alkaline Carbonate Stress Corrosion Cracking | NO
8 | SCC – Polythionic Acid Stress Corrosion Cracking | NO
9 | SCC – Chloride Stress Corrosion Cracking | NO
10 | SCC – Hydrogen Stress Cracking-HF | YES
11 | SCC – HIC/SOHIC-HF | YES
12 | External Corrosion – Ferritic Component | NO
13 | Corrosion Under Insulation—Ferritic Component | NO
14 | External Chloride SCC—Austenitic Component | NO
15 | External Chloride SCC Under Insulation—Austenitic Component | NO
16 | High Temperature Hydrogen Attack | YES
17 | Brittle Fracture | NO
18 | Low Alloy Steel Embrittlement | NO
19 | 885 °F Embrittlement | NO
20 | Sigma Phase Embrittlement | NO
21 | Piping Mechanical Fatigue | NO
depends on the damage mechanism!
Notes: Talk about the D mechanisms In API RBI 581

## Slide 16
Risk-Based Inspection
Damage Mechanisms API581 | 
1 | SCC – Sulfide Stress Cracking
2 | SCC – HIC/SOHIC-H2S
3 | SCC – Hydrogen Stress Cracking-HF
4 | SCC – HIC/SOHIC-HF
5 | HTHA - High Temperature Hydrogen Attack
HTHA:
Decarburization process at high temperatures
SCC:
Stress corrosion cracking
SCC is a form of HSC resulting from the absorption of atomic hydrogen that is produced by the corrosion process on the metal surface [7]
Steel structure
Notes: Difference between HTHA and SCC, talk about why we chose SCC and not HTHA. The reason for the hydrogen uptake is different (corrosion process) but there is an uptake of atomic hydrogen in the material. Different magnitude of consequences, different time dependency of the phenomena but at the end of the day is still dissolved atomic hydrogen combined with stress of the material that causes failure.

## Slide 17
Risk-Based Inspection
Damage Mechanisms API581 | 
1 | SCC – Sulfide Stress Cracking
2 | SCC – HIC/SOHIC-H2S
3 | SCC – Hydrogen Stress Cracking-HF
4 | SCC – HIC/SOHIC-HF
5 | HTHA - High Temperature Hydrogen Attack
Effect of atomic hydrogen production at a crack tip for different environments [9]

## Slide 18
Methodology
Synergi Plant RBI [8] – developed by DNV
SCC – HIC/SOHIC-H2S
Probability of Failure
Damage Factor
Notes: Talk about synergi. Talk about PoF calc.

## Slide 19
Methodology
SCC – HIC/SOHIC-H2S
Consequence of Failure
Input for CoF - Screening Procedure for hydrogen release |  | 
NFPA Flammability | 4/4 | Extremely flammable
NFPA Toxicity | 0/4 | Not Toxic
Personnel Injury | 5/5 | Any fatality or significantly public minor injury possible
Environmental Consequence | 5/5 | Any fatality or significantly public minor injury possible
Business Impact | 5/5 | More than 5 days production loss plus maintenance costs
Operating Pressure Range | ≥ 40 bar | 
Operating Temperature Range | ≤ 38 °C | 
Mass Release | ≤ 450 kg | 
Synergi Plant RBI [8] – developed by DNV
Notes: Talk about CoF calc in synergi. The quantitative approach requests the setting of a series of parameters not assessable at a preliminary design stage (number of injuries, casualties, business loss, etc.).

## Slide 20
Results and Discussion
SCC – HIC/SOHIC-H2S
Probability of Failure
Damage Factor
Notes: These are the result if we consider SOHIC for our hydrogen cylinders.

## Slide 21
Results and Discussion
SCC – HIC/SOHIC-H2S
Probability of Failure
Damage Factor
evaluation considering medium susceptibility
evaluation considering high susceptibility
Notes: Bypass of the environmental conditions

## Slide 22
Results and Discussion
Steel structure
HE is enhanced at higher pressures
Notes: Recap.

## Slide 23
Conclusions
The application of the existing RBI 581 [7] procedures as they are to hydrogen technologies can lead to a risk underestimation.
The output of these procedures mainly rely on the expertise of the user.
The damage mechanisms involving hydrogen in RBI 581 are not suitable for equipment working in pure hydrogen environments.
Specific RBI methodology should be developed for these systems.
Inspection Planning in the Marine Sector: a Case Study of a Hydrogen-Fueled Fishing Vessel

## Slide 24
Thank you for your attention!
For further details please contact me:
OMAE 2023 – 42nd International Conference on Ocean, Offshore & Arctic Engineering
Melbourne Convention and Exhibition Centre, Melbourne, Australia
June 11-16, 2023
Leonardo Giannini: leonardo.giannini@ntnu.no

## Slide 25
Bibliography
OMAE 2023, 42nd International Conference on Ocean, Offshore & Arctic Engineering, https://event.asme.org/OMAE
International Maritime Organization, Fourth IMO GHG report, IMO, 2020, https://www.imo.org/en/OurWork/Environment/Pages/Fourth-IMO-Greenhouse-Gas-Study-2020.aspx
Statistics Norway, Emissions to air (Table 09288: Greenhouse gases from Norwegian economic activity, by industry, pollutant, contents and year), https://www.ssb.no/en/statbank/table/09288/tableViewLayout1/
Sepideh Jafarzadeh et al., Electrification of the coastal fishing fleet using batteries and fuel cells (Elektrifisering av kystfiskeflåten ved bruk av batterier og brenselceller), Sintef Ocean, 2021, https://www.fhf.no/prosjekter/prosjektbasen/901640/.
A. Alvaro. “3D cohesive modelling of hydrogen embrittlement in the heat affected zone of X70 steel”. PhD thesis. 2014. ISBN: 978-82-326-5575-5.

## Slide 26
Bibliography
American Petroleum Institute, Risk-Based Inspection, API Recommended Practice 580, 2016.
American Petroleum Institute, Risk-Based Inspection Methodology, API Recommended Practice 581, addendum 1, 2019
DNV, Synergi Plant RBI, https://www.dnv.com/services/rbi-software-risk-basedinspection-synergi-plant-4666.
R.P. Gangloff, “Hydrogen Assisted Cracking of High Strength Alloys”, In: Comprehensive Structural Integrity 6, 31-131 (2003).